## Slide 1: HomeAutomation
By: Christopher Matthews

## Slide 2: HomeAutomation
Project Goals
  Setup Home Automation using Alexa Device or Web Interface
Purpose
  Create a voice controlled device that does not require some subscription, signup or any other action other than connect and operate

## Slide 3: Circuit Diagram
Red: Live Wire
Blue: Comms Connection
Black: Ground Wire
Components:
ESP8266 MicroController
Relay Controlled Switch
Power Converter
Mains Power

## Slide 4: ESP8266 Microcontroller
ESP8266
  Wireless interface
  Bluetooth
  Programmable through Arduino IDE
  C and C++ programming

## Slide 5: HomeAutomation
Libraries
  #include "ESP8266WiFi.h“ -> Enables the WiFi on the Chip
  #include "ESP8266WebServer.h“ ->WebServer setting
  #include "WiFiManager.h“ ->Control WiFi Settings on Boot
  #include "DNSServer.h“ -> To setup DNS name
  #include "fauxmoESP.h“ -> Allows for Alexa Integration

## Slide 6: HomeAutomation
Setting up the ports and control commands
  fauxmoESP homeDevice; ->Starts the service for Alexa App
  uint8_t relay =14; -> Sets GPIO pin 14 as the DO for the Relay
  ESP8266WebServer server; ->Starts the webserver
  DNSServer dnsServer; ->Sets up the DNS Server
  WiFiClient espClient; ->Creates the WIFI Client object
  #define switch “light“ ->Sets the listening command
  pinMode(relay, OUTPUT); ->Sets the pin mode of the DI/DO to DO
  digitalWrite(relay, LOW); ->Sets the relay to low at start which is off

## Slide 7: HomeAutomation
Setting up the WiFi Automatically
  Serial.begin(115200); -> For debugging purposes only
  WiFiManager wifiManager; ->Creates a WiFi Manager object
  wifiManager.resetSettings(); -> set to default
  wifiManager.autoConnect("LightingPLC");->creates name
  Serial.print("IP Address: "); >output IP to Console
  Serial.println(WiFi.localIP()); -> output IP to Console
  Serial.println(WiFi.subnetMask());->outputs Subnet to console

## Slide 8: HomeAutomation
Setting up the server and services
  homeDevice.createServer(true);
  homeDevice.setPort(80); ->Using HTTP protocol
  server.on("/", handleRoot); -> Sets homepage for Internal Server
  server.on("/toggle", toggleRelay); ->Calls toggle Function to switch on/off
  server.begin(); ->Starts the Internal Server
  homeDevice.enable(true);
  homeDevice.addDevice(switch);

## Slide 9: HomeAutomation

## Slide 10: HomeAutomation